Vibro-Acoustics Guideline Master: Grille Silencer Specifications

[INSERT THIS SECTION IN PART 2 – PRODUCTS OF THE APPROPRIATE SECTION WITHIN DIVISION 15, MECHANICAL SYSTEMS]

2.XX	GRILLE SILENCERS

2.XX.1	Grille silencers shall be constructed with minimum 22 gauge galvanized steel frames and outer casings.

2.XX.2	Acoustical fill shall be bacteria and fungus resistant, glass fiber acoustic media.  Glass fiber thickness and density shall be as required to insure conformance with laboratory test data.

2.XX.3	Acoustical fill shall be faced with an acrylic polymer coating. The coating shall include a protective agent to guard against microbial growth.

2.XX.4 Grille silencers shall have clean and neat appearance as required for visual acceptance.  All  steel shall be adequately stiffened to insure flatness and form.  All spot welds shall be painted.

2.XX.5	Grille silencer acoustical and aerodynamic performance shall be as indicated on the schedule.

2.XX.6	Grille silencer acoustical performance shall be determined per ASTM E90-02.  Grille silencer aerodynamic performance shall be determined per AMCA Standard 500-L-99.  Manufacturer shall submit certified data substantiating both the specified acoustic and aerodynamic performance.

2.XX.7	Grille silencers shall have flame-spread index not exceeding 25 and smoke-developed index not exceeding 50 when tested according to ASTM E 84, NFPA 255 or UL 723.

2.XX.8	Acceptable manufacturers: Vibro-Acoustics (basis of design).